## Slide 1
ENVIRONMENTAL SCIENCES &
FIELD SERVICES DIVISION
Daniel George
Isaac Schmidt
PACE ANALYTICAL

## Slide 2
Why Collecting Viable Samples Matters
Leachate Sampling Scenarios
Groundwater Sampling Scenarios
PFAS & Sampling Suggestions
Compounds of Emerging Concern
Field Documentation & Resources
AGENDA
How to Collect Viable Leachate and Groundwater Samples

## Slide 3
Why Collecting Viable Samples Matter
Health of Landfill
-Leachate is a key end product of the reactions taking place within the landfill between solid waste, microorganisms, and moisture.
-Various laboratory analysis including BOD5, COD, ammonia, pH, and TSS can help characterize the landfill
-Degree of stabilization –Point towards problems of groundwater ingress, excessive recirculation, or presence of unusual wastes
-Following improper procedures can skew analytical data obtained from samples, leading to an inaccurate characterization
-Good sample collection procedures matter so the data collected is an accurate characterization
2
Permit Compliance
-Ensures that leachate data falls within parameters outlined by the permitting body
-Determine if the landfill is functioning properly
-Determine if leachate is suitable for off-site transport and disposal or application
1

## Slide 4
Leachate Monitoring Scenarios
Leachate Collection Well
1
2
3
4
Storage Tanks
Leachate Pond
Post Application Monitoring Well

## Slide 5
Leachate Collection Well
Proper Collection Technique & Equipment
Low Flow Pump and Sample Cell
  Helps with Recharge
  Don’t need to purge a large volume
Field Parameters Near Stable
Teflon Tubing
Make sure sample collection does not overly agitate leachate
Also make sure collection is not just from the top portion of leachate in well
  Top portion may have volatilized
  Bottom may contain unrepresentative sludge/solids
Notes: Low Flow Sampling – Using Peristaltic pump/bladder pump. This allows for proper recharge of monitoring well and ensures a representative sample. Purging to fast, damage pump, draw down the well to fast and draw unrepresentative solids. Low flow allows for a large amount of volume to be purge. 3 Volume Pruge Less Then .5 LPM

## Slide 6
Storage Tanks/Leachate Pond
Proper Collection Technique
Teflon Tubing
Make sure sample collection does not overly agitate leachate
Also make sure collection is not just from the top portion of leachate in tank, utilize bailer or pump to get a representative sample
VOC procedures
  Turn off your vehicle
  Don’t use products that contain VOCs prior to sampling
  Wear proper gloves
  Fill glass bottle as direct as possible

## Slide 7
Post Application Monitoring Well
Proper Collection Technique
Low Flow Pump and Sample Cell
  1 LPM purge rate taking a field reading every 5 minutes
  Field Parameters – Using YSI Pro Plus
Teflon Tubing
Dedicated field monitoring pumps, Don’t need to worry about field sampling procedures affecting results.
Notes: Dedicated pumps – cost effective, low maintenance, can last up to 10 years if taken care of properly. If water is to turbid it can hard the pump

## Slide 8
Filling Lab Bottles
Proper Collection Technique
Filling VOC vials
  Leachate reacts with preservative and causes foam. Bubbles are ok but only want approximately 6 mm in diameter of total
Be aware of bottles containing preservatives
Fill bottles to neckline
If sample is known to have a high or low pH let the lab know
Notes: When collecting from a pond use a glass transfer device, plastic bottles may contain/leach trace VOCs, especially with volatile nature of leachate. Want to fill 40 mL vials as direct/fast as possible so VOCs don’t

## Slide 9
Lack of federal regulation
Non-uniformity of state regulation
Non-uniformity of test methods
Lack of environmental test methods
Variety of compound lists
Thousands of PFAS compounds
Low DLs vs contaminated matrices
Ultra restrictive field sampling guidance
All this conspires to lead to uncertainty & a highly consultative process
PFAS is the Wild West

## Slide 10
Per- and polyfluoroalkyl substances (PFAS) are a large, diverse group of manufactured compounds used in a variety of industries:
Aerospace, automotive, apparels, food packaging, fire-fighting foams, non-stick coatings/cookware, carpeting & metal plating
PFAS are anthropogenic chemicals and do not occur naturally in the environment.
Phonetically: PFAS = PF +
Overview

## Slide 11
Textiles and Leather: factory and consumer applied coating to repel water, oil, and stains
Paper Products: surface coatings to repel grease and moisture
Metal Plating and Etching: corrosion prevention, wear reduction, surfactant, fume suppressant
Wire Manufacturing: coating and insulation
Pesticides, cleaning products, polishes, photo processing
Common Sources

## Slide 12
Wastewater Treatment
Consumer and industrial use of PFAS-containing materials, including disposal of landfill leachate and firefighting foam, results in the discharge of PFAS to wastewater treatment plants (WWTPs). NE states are working to establish regulations to limit PFOA & PFOS to WWTP.
WWTP Operations
Conventional sewage treatment methods do not efficiently remove PFAS
Conventional treatment processes can change PFAS concentrations
  Increase in PFAA due to transformation of precursor PFAS
PFAS in Water

## Slide 13
WWTP Biosolids
PFAS have been found in domestic sewage sludge
More than half of the sludge produced in the United States is applied to agricultural land as biosolids
Application of biosolids as a soil amendment can result in a transfer of PFAS to soil
PFAS can enter the food chain through the use of biosolids-amended soil
PFAS concentrations can be elevated in surface and groundwater in the vicinity of agricultural fields that received PFAS contaminated biosolids
Not just in water

## Slide 14
Additionally, DoD QSM 5.3 newest method 533 which is isotope dilution.
PFAS Methods

## Slide 15
PFAS Monitoring
Proper PFAS Collection Technique
Test Prep
  Clean pumps
    Laboratory supplied PFAS free deionized water
  New/dedicated Tubing (HDPE Tubing)
  Confirm additional sampling equipment is PFAS free or has been decontaminated
  Easy to use FDS which help keep track of notes/results
PFAS Sampling
  Collect PFAS Sample First
  Don’t place sample bottle cap on any surface
  Do not use Teflon Tubing, HDPE Tubing is preferred
  Place each sample in a plastic bag.
  It is recommended to use Field Reagent Blanks (FRB)

## Slide 16
Fluorotelomers – part of PFAS family – AFFF
Microbeads/Microplastics
Pharmaceuticals in GW
Contaminants of emerging Concern

## Slide 17
Chain of Custody & Why It Matters
Proper Collection Technique
Fill out COC completely
  Client/contact information
  Use permit related Sample ID when necessary
  Double check analytical parameters
  Turn Around Time (TAT)
The more information the better
Pack your cooler properly
  Helps ensure samples are received in the proper testing condition
  Loose ice is most effective means to keep samples coolest in the cooler, which is cool.
Fill out any field sheets with notes and observations
Improperly filled out COC could cause delay in analytical results

## Slide 18
Resources

## Slide 19
THANK YOU